## Slide 1
EWS LANDSLIDE
The severity numbers
on the dashboard
A simple walkthrough — no technical background required
1
What they are
2
How they're calculated
3
What changes them
EWS Landslide · Severity Numbers
1 / 7

## Slide 2
BACKGROUND
The EWS Landslide System
Sensors in the field monitor landslide-prone sites 24/7.
They measure rainfall, ground vibration, tilt, and cracks.
The system combines all of these to assign a severity number to each site.
STEP 1
4 Sensors
Rain, vibration,
tilt, crack
STEP 2
15-minute updates
Fresh data every
15 minutes
STEP 3
15 Sites
Nodes Alpha through
November
EWS Landslide · Severity Numbers
2 / 7

## Slide 3
WHAT YOU SEE ON THE DASHBOARD
Three states: Green, Yellow, Red
Each node card shows one of three status colors based on a score from 0 to 20.
0 – 3
NORMAL
Light rain. Quiet site. No alerts.
3 – 10
WARNING
Above-average rain. Site is active.
10 – 20
CRITICAL
Heavy rain or peak readings. Full alert.
EWS Landslide · Severity Numbers
3 / 7

## Slide 4
THE MATH
How the number is calculated
Two steps. That's all.
Step 1: Normalise
score = raw_value ÷ 80
The sensor capacity is 80 tips per 15 minutes.
If the sensor shows 52, the score is 52 ÷ 80 = 0.65
Step 2: Scale
severity_score = score × 20
Multiply by 20 so we get a number between 0 and 20.
0.65 × 20 = 13.0 → shows as 13.00 on the card
Quick reference: raw 10 → 2.5 | raw 25 → 6.25 | raw 40 → 10.0 | raw 64 → 16.0 | raw 80 → 20.0
EWS Landslide · Severity Numbers
4 / 7

## Slide 5
DASHBOARD VS ALERTS
Two numbers, two jobs
The score you see on the card is NOT what decides who gets SMS. They are two separate systems.
The Dashboard Score (what you see)
Range:
0 to 20 (decimal, e.g. 13.00)
Formula:
raw_value ÷ 80 × 20
Colors:
Green 0–3 · Yellow 3–10 · Red 10–20
Purpose:
Show the operator a real-time value
Calls anyone?:
No
The Alert Trigger (who gets notified)
Range:
0, 1, 2, 3 (integer, never decimal)
Formula:
max(hardware_thresholds, ML_probability)
Meaning:
0: quiet · 1: email · 2: +SMS · 3: all admins
Purpose:
Decide who gets notified, and how fast
Calls anyone?:
Yes — SMS to operators and admins
Key insight: 13.00 on the card tells you WHAT is happening. Alert trigger = 2 tells you WHO is being told.
EWS Landslide · Severity Numbers
5 / 7

## Slide 6
TRIGGERS
What changes the score on the card?
Only four things. No hidden cron jobs. No manual overrides.
1
A new sensor reading arrives
Every 15 minutes the sensor sends fresh data. The formula recalculates instantly.
Raw 52 → score 13.0. Raw 64 → score 16.0. New rain = new number.
2
The formula denominator changes
If the sensor capacity is upgraded from 80 to 100, the same rain reads lower.
Raw 52 → 52 ÷ 100 × 20 = 10.4 instead of 13.0. Rare.
3
The color-band thresholds are updated
The ops team can change when a card goes from green to yellow (default: 3)
or yellow to red (default: 10). Changes colors, not the score.
4
Demo data is injected
The team can simulate readings that walk the score from 0 to 20 for training.
Never happens during real operations.
What does NOT change it: cron jobs, manual typing, magic.
EWS Landslide · Severity Numbers
6 / 7

## Slide 7
RECAP
Summary
Three takeaways.
The score is simple.
raw_value ÷ 80 × 20 = 0 to 20. Three bands: green 0–3, yellow 3–10, red 10–20.
Two systems work side by side.
Dashboard score shows you the state. Alert trigger (0–3) decides who gets SMS.
Numbers only change when new data arrives.
Every 15 minutes from the sensor. No cron. No manual override. No hidden clock.
The dashboard score only shows rain. Tilt, vibration, and crack are evaluated by the alert trigger separately.
Trust the dashboard to show you what's happening. Trust the operators to decide what to do.
EWS Landslide · Severity Numbers
7 / 7