## Slide 1
Landslide Early Warning System
IoT • Machine Learning • SaaS
Riset Lab IoT
Universitas Padjadjaran
Bandung, Indonesia • 2026
Prototype Design
5 Nodes + Gateway
LoRaWAN + ML
Solar Powered

## Slide 2
Latar Belakang
Masalah Longsor di Bandung dan Kebutuhan Sistem Peringatan Dini
Permasalahan
Bandung rural memiliki risiko longsor tinggi (musim hujan Oktober–Maret)
Monitoring manual tidak mampu mendeteksi pergeseran lereng secara real-time
Sistem EWS komersial berharga mahal (Rp 50M+ per node industri)
Kurang akses internet di pedesaan membatasi solusi berbasis cloud saja
Solusi yang Diusulkan
IoT sensor nodes dengan LoRaWAN (jarak jauh, hemat daya)
Prototipe student-grade untuk riset (biaya < Rp 1Juta/node)
ML cloud-side untuk deteksi anomali dengan akurasi tinggi
SaaS dashboard multi-tenant untuk monitoring real-time
Target Area: Desa-desa rural Bandung (Lembang, Rancabolang, Ciburial)

## Slide 3
Arsitektur Sistem
High-Level Overview: IoT → ML → SaaS
Sensor Nodes (Edge)
ESP32-S3 + RFM95W LoRaWAN + Solar
LoRaWAN Gateway
RPi Zero2 W RAK/LoRa HAT
The Things Network
MQTT Webhook Free Tier
Cloud Backend (ML + API)
FastAPI + TimescaleDB scikit-learn
SaaS Dashboard (Frontend)
Next.js Real-time Alerts
Data Flow: Sensor Readings → LoRaWAN TX → TTN → Webhook → FastAPI → TimescaleDB → ML Inference → Alert Engine → SMS/Email
Edge Layer (Hardware)
• 5× ESP32-S3 sensor nodes • 1× LoRaWAN gateway • 10W solar panel per node • 3× 18650 battery (26-day autonomy)
Cloud Layer (Backend)
• FastAPI REST + WebSocket • TimescaleDB • scikit-learn Random Forest • Alert Engine (Twilio SMS + Email)
Application Layer (Frontend)
• Next.js SaaS dashboard • Leaflet map • Real-time charts (Recharts) • Multi-tenant + role-based access

## Slide 4
Arsitektur Hardware
Per Node: ESP32-S3 + Sensor Suite + Solar Power
Komponen per Node
MCU
ESP32-S3 DevKit C — dual-core, deep sleep 10µA
LoRa
RFM95W 915MHz — LoRaWAN AS923 band
Rain
MH-RD Tipping Bucket — interrupt on tip
Accel
GY-521 MPU-6050 — I²C, vibration threshold
Tilt
GY-25 UART — calibrated ±80°, 0.01° resolution
GPS
u-blox NEO-6M — periodic position check 1-6h
Ext.
Slide Potentiometer 10kΩ — crack displacement
Power
3× 18650 + TP4056 + 10W Solar + Controller
Profil Daya (Hybrid Mode)
Deep Sleep
~10 µA
MCU idle, sensors in standby
Scheduled Wake
~20 mA × 5s
Poll sensors + LoRaWAN TX every 15 min
Interrupt Wake
~20 mA × 3s
Rain tip / accel spike → immediate TX
Solar Recovery
10W panel
~4-5 hours partial sun → full charge
Battery Autonomy
26 days
3×18650 (6600mAh) / 250mAh/day
Battery Life: 2–3 Years (est.) — exceeds 3-5 day autonomy requirement

## Slide 5
Bill of Materials — Per Node
Student-Grade Prototype Hardware
Komponen
Produk
Harga (Rp)
Qty
Subtotal (Rp)
MCU
ESP32-S3 DevKit C
85,000
1
85,000
LoRa Radio
RFM95W 915MHz
80,000
1
80,000
Rain Sensor
MH-RD Tipping Bucket
15,000
1
15,000
Accelerometer
GY-521 (MPU-6050)
25,000
1
25,000
Inclinometer
GY-25 (UART)
120,000
1
120,000
GPS Module
u-blox NEO-6M
80,000
1
80,000
Extensometer
Slide Potentiometer 10kΩ
20,000
1
20,000
Power
18650 LiPo ×3 + TP4056 + Solar
225,000
1
225,000
Casing
IP65 Junction Box
40,000
1
40,000
Wiring/PCB
Jumper, perfboard, connectors
40,000
1
40,000
Per Node Total
~Rp 730,000
5 Nodes Total
~Rp 3,650,000

## Slide 6
Protokol Komunikasi
LoRaWAN MAC + Custom Binary Payload
LoRaWAN Stack (MCCI Library)
Region
AS923 — Indonesia 915MHz band
MAC Version
1.0.3 (LoRaWAN Regional Parameters)
Adaptive Data Rate
Enabled — auto-optimizes TX time
Duty Cycle
1% regulatory limit (max 36s/hr)
TX Power
14 dBm max (adjustable)
Security
AES-128 end-to-end encryption
Protocol
MCCI LoRaWAN + The Things Stack
Integration
MQTT / HTTP Webhook → FastAPI
Custom Binary Payload (19 bytes)
MSB ──────────────────────────────────► LSB
1B Severity Flag
0x00=Normal, 0x01=Watch, 0x02=Warning, 0x03=Critical
1B Sensor Mask
Which sensors are reporting in this burst
2B Rain Tips (15min)
Cumulative tipping bucket count
2B Accel Magnitude
RMS g-force over window (×0.001g)
2B Tilt Angle (°)
Deviation from baseline (×0.01°)
2B Crack Delta (mm)
Displacement from baseline (×0.1mm)
4B Latitude
Signed 32-bit × 10⁶ (degrees)
4B Longitude
Signed 32-bit × 10⁶ (degrees)
2B Battery (mV)
MCU supply voltage × 1mV resolution
Benefits: 19-byte payload = ~100ms TX time → ultra-low power • Binary format = no JSON parsing overhead on MCU • Severity flag enables gateway-level priority routing

## Slide 7
Manajemen Daya
Hybrid Mode: Scheduled + Interrupt-Driven
Scheduled Wake (every 15 min)
~250 µAh/day
• MCU wakes, polls all sensors (~3-5s)
• LoRaWAN TX with current readings
• Returns to deep sleep (10µA)
• Captures slow-deformation trends
Interrupt Wake (Emergency)
~50 µAh/day
• Rain tip → immediate wake, burst TX
• Accel >0.2g sustained → wake, TX
• Tilt >2° change → wake, TX
• Overrides schedule for critical alerts
Solar Charging (10W panel)
Full charge 4-5 hours sun
• 10W monocrystalline panel
• MPPT controller for efficiency
• 3× 18650 in parallel (6600mAh)
• Survives 3-5 cloudy days (industry std)
Power Budget Summary
Daily: ~300µAh | Battery: 6600mAh | Autonomy: 22+ days | Solar recovery: 4-5h partial sun | Battery life: 2-3 years (est.)

## Slide 8
Arsitektur Gateway
LoRaWAN Gateway: Raspberry Pi Zero2 W + Solar
Gateway Components
RPi Zero 2 W
Quad-core ARM, WiFi/Ethernet
Rp 250,000
LoRa HAT
RAK2245 / DoIT 8-ch gateway
Rp 450,000
Antenna
915MHz 3dBi outdoor • IP66
Rp 100,000
Power
5V adapter + UPS hat + Solar 10W
Rp 300,000
Casing
IP66 outdoor enclosure
Rp 200,000
Total
Rp 1,300,000
Gateway Data Flow
1
LoRa RX
Sensor nodes transmit via LoRaWAN to gateway
2
De-duplicate
Gateway filters duplicate frames (multi-channel)
3
TTN uplink
Forward to The Things Stack via MQTT
4
Webhook
TTN forwards to FastAPI backend via HTTPS
5
Internet
RPi Zero2 W connects via WiFi/Ethernet to cloud
Coverage: ~5km urban, ~15km rural (line-of-sight) — covers most village pilot areas

## Slide 9
Arsitektur Backend
FastAPI + TimescaleDB + ML Inference Service
Data Ingestion
TTN MQTT Webhook → FastAPI
Decode binary payload (19B)
Validate → TimescaleDB write
Storage
TimescaleDB (PostgreSQL ext)
Retention: 30 days raw, 1yr aggregated
Compression: ~10:1 ratio
ML Inference
scikit-learn Random Forest
Input: tabular sensor features
Output: landslide probability 0-1
Alert Engine
Rule-based thresholds OR ML P>0.7
Escalation: Watch → Warning → Critical
Dispatch: SMS (Twilio) + Email
API / Frontend
FastAPI REST + WebSocket
Next.js dashboard (real-time)
JWT auth + multi-tenant
Tech Stack
FastAPI 3.11+
TimescaleDB
scikit-learn
Twilio SMS
Next.js 14
Socket.IO
JWT Auth
DigitalOcean VPS

## Slide 10
Pendekatan Machine Learning
Cloud-Side Anomaly Detection — dari Random Forest ke LSTM
Fase 1 — Random Forest Classifier
Input Features (6)
Rain tips 15min • Accel RMS • Tilt delta • Crack delta • Time-of-day • Season
Target Label
0 = Normal, 1 = Pre-landslide pattern (synthetic initially)
Why Random Forest?
Interpretable • Fast inference (<100ms) • No GPU needed • Robust to noise
Training Data
Start: synthetic threshold violations → Real: labeled historical sensor data
Output
P(landslide) in next 1-hour window • Threshold: >0.7 = Critical alert
Fase 2 — LSTM / GRU (Upgrade)
Input Features
Time-series window (e.g., 24 readings × 6 features)
Why LSTM?
Captures temporal patterns: slow creep → acceleration → failure
Architecture
2-layer LSTM (128 units) + Dense → output P(landslide)
Training Data
Requires 3-6 months labeled historical data (normal + event)
When to upgrade
After collecting 6+ months real data AND RF accuracy plateaus
Model Comparison
Random Forest
LSTM
Rule-based only
Inference Speed
< 100ms
50-200ms
< 1ms
Data Required
500+ samples
10,000+ samples
None
Interpretability
High (feature importance)
Medium
Very high
GPU Required
No
Yes (or cloud)
No

## Slide 11
Alert Engine
Two-Stage Logic: Hardware Threshold + ML Probability
Stage 1: Hardware Threshold
• Rain tips > 10 in 15 min → Severity 0x01 (Watch)
• Tilt deviation > 5° from baseline → Severity 0x02 (Warning)
• Accel > 0.3g sustained 2s → Severity 0x02 (Warning)
• Multi-sensor violation → Severity 0x03 (Critical)
Stage 2: ML Probability
• ML P > 0.5 → Escalate severity by 1 level
• ML P > 0.7 → Critical alert (0x03), immediate SMS
• Combined: Hardware OR → ML = Alert trigger
• Reduces false positives vs threshold-only system
Notification Rules
Severity
Dashboard
Email
SMS
0x01 Watch
Log only
No alert
No alert
0x02 Warning
Dashboard alert
Email operators
No SMS
0x03 Critical
Dashboard + siren
Email + SMS
Immediate
SMS via Twilio/Nexmo — Indonesian local number preferred for cost. Dashboard uses Socket.IO for real-time push.

## Slide 12
Frontend SaaS Dashboard
Next.js — Real-time Monitoring + Alert Management
Real-time Monitoring
Live sensor readings per node via WebSocket, auto-refresh charts
Map View
Geographic visualization with Leaflet + OpenStreetMap, severity color-coding
Alert Management
Acknowledge/resolve workflow, severity levels, alert history
Node Management
Add, configure, calibrate sensor nodes, set per-node thresholds
Data Export
CSV/JSON export, date-range filter, historical data explorer
Multi-tenant Access
Role-based: Admin (full) / Operator (acknowledge) / Viewer (read-only)
Built with:
Next.js 14 (App Router)
Tailwind CSS
Recharts
Leaflet + OSM
Socket.IO
NextAuth.js

## Slide 13
Biaya Operasional
Hardware Investasi + Biaya Bulanan Berkelanjutan
One-Time Hardware Investment
5× Sensor Nodes
Rp 3,650,000
1× LoRaWAN Gateway
Rp 1,300,000
Mounts, cables, misc
Rp 500,000
Total Hardware
~Rp 5,450,000
vs Industrial Grade:
Student-grade = 95% cost reduction
Monthly Recurring Cost
Cloud VPS (backend + DB)
Rp 80,000
~$2.5/mo (DigitalOcean)
SMS Alerts (Twilio)
Rp 50,000
~$1.5/mo (50 critical alerts)
Email (SendGrid)
Rp 15,000
~$0.5/mo
Domain + SSL
Rp 0
Cloudflare + Let's Encrypt
TTN Community
Rp 0
Free tier
Monthly Total
~Rp 145,000
Year 1 Total
Hardware (Rp 5.45M) + Ops (Rp 1.74M) = ~Rp 7.2M
Per-node/year (Y2+): ~Rp 1,200,000 (~USD 72)

## Slide 14
Timeline Implementasi
5 Fase — 11-16 Minggu Total
Fase 1 Edge Firmware
2-3 minggu
• Design binary payload
• LoRaWAN stack on ESP32-S3
• Sensor polling code
• Hybrid sleep + interrupt
• Power profiling test
Fase 2 Backend Infra
3-4 minggu
• VPS setup + TimescaleDB
• TTN deployment
• FastAPI ingestion + WebSocket
• ML Random Forest baseline
• Alert engine + SMS
Fase 3 Frontend SaaS
3-4 minggu
• Next.js scaffold + Tailwind
• Auth (JWT + roles)
• Dashboard + charts
• Map + node management
• Data export
Fase 4 Field Testing
2-3 minggu
• Deploy 5 nodes + gateway
• Collect baseline data
• Simulate failure scenarios
• ML model tuning
• Stakeholder user testing
Fase 5 Documentation
1-2 minggu
• System architecture doc
• ML methodology writeup
• Cost/benefit analysis
• Lessons learned
Total: 11-16 minggu | Immediate action: Build 1 prototype node + test LoRaWAN coverage in backyard

## Slide 15
Verifikasi dan Testing
End-to-End System Validation
Hardware Verification
Deep sleep current < 15µA (multimeter)
TX current < 120mA peak (oscilloscope/multimeter)
LoRaWAN packet delivery > 95% (100-packet test)
Solar charging: cloudy day sim → battery drain < 20%
Rain sensor tip interrupt response < 100ms
Backend Verification
API endpoint tests → 200 OK for all routes
WebSocket connection → real-time data to frontend
ML inference latency < 100ms per message
SMS delivery → alert received < 30s of trigger
TimescaleDB retention policy → data auto-archived
End-to-End Verification
Simulate landslide: manual tilt + rain bucket trigger
Verify: severity flag → TTN → webhook → ML → alert → SMS
Dashboard shows alert within 60s of trigger
SMS received by operators within 90s
Alert resolved → dashboard updates in < 5s
Key Metric: Sensor trigger → Dashboard alert < 60s | Operator SMS < 90s | End-to-end reliability > 95%

## Slide 16
Risiko dan Mitigasi
Identifikasi Risiko Utama + Strategi Penanganan
Risiko
Dampak
Mitigasi
Status
LoRaWAN coverage gaps
Sensor data not reaching gateway
Build own solar gateway (included in BOM), test coverage before deployment
Mitigated
Power drain during rainy season
Battery dies during critical event
3×18650 + 10W panel = 26-day autonomy, far exceeds requirement
Mitigated
False positives from sensor noise
Alarm fatigue, unnecessary alerts
Two-stage alert: hardware threshold + ML probability filter
Mitigated
SMS delivery failure
Critical alert not received
Redundant email + dashboard; test Indonesian provider before field
Monitoring
Vandalism / theft
Hardware damaged or stolen
Camouflage casing; community involvement; local govt partnership
Open
ML model low accuracy (no labeled data)
False negatives = missed events
Start with rule-based thresholds; ML improves as labeled data accumulates
Open

## Slide 17
Kesimpulan dan Langkah Selanjutnya
Ringkasan Sistem
LoRaWAN IoT sensor nodes dengan solar power — desain ultra-low power
Custom binary payload dengan severity flag — minimal TX time
Hybrid sleep mode (scheduled + interrupt) — 26-day battery autonomy
Cloud ML dengan Random Forest → upgrade path ke LSTM
Two-stage alert engine: hardware threshold + ML probability
Next.js SaaS dashboard multi-tenant — real-time monitoring + alerts
Biaya prototipe ~Rp 5.45M dengan biaya operasional ~Rp 145K/bulan
95% lebih murah dari solusi industrial-grade dengan arsitektur yang sama
Langkah Selanjutnya
1. Finalisasi lokasi pilot village
2. Pesan hardware + assemble prototype node
3. Test LoRaWAN coverage (backyard/gateway)
4. Deploy backend di VPS (DigitalOcean)
5. Mulai pengumpulan data baseline
6. Train & validate ML model
Riset Lab IoT — Universitas Padjadjaran — Landslide Early Warning System — 2026